12.03.2018y.
MDADM + install Lubuntu Alternate on RAID0
Mdadm is useful package for making software disk array software controller. Please refer to user manual ( #man mdadm ). Please refer to these commands for providing non system-bootable disk for separate data IO, or swap area:
1) install mdadm package:
#sudo aptitude install mdadm
2) cut every disk to constant size with Gparted Graphical User Interface:
#sudo aptitude install gparted && sudo gparted
    Device->Create Partition Table -> msdos
    Partition->New->#ConstantSizeOnEachDisk
#sudo mdadm --create --verbose /dev/md0 --level=0 --raid-devices=X /dev/sdx /dev/sdy /dev/sdz …
install Lubuntu Alternate on software RAID0
RAID 0 is non-disk-failure-robust disk array implementation providing simplest and fastest solution for multiple disk utilization. One can configure and install system on such solution. Most motherboard supports up to 2-3GBps throughput for all peripheral ports. In such system software disk array provides quite good results with capacity, price, real Read/Write throughput, and kIOps/GB. On the other hand it would be cheaper to use efficiently M.2 disks – but this technology is not popular, and still expensive nowadays. At beginning of 2018y. capacity optimal are: used 3.5’’ SATA( 4 – 6 pieces )/PATA( 4 pieces ) HDD’s, 7.2krpm, 8MB SRAM cache, 80-250GB ( for example 6x160GB ) via 512B/disk sequential accesses. Pseudo random access optimal is usage of 2.5’’ SATA( 2 – 4 pieces ) SSD’s, 120GB via 4kB/disk sequential accesses.
1) download Lubuntu Alternate, and make bootable pendrive via Startup Disk Creator, or UNetBootIn:
https://lubuntu.net/downloads/
2) install in an ordinary way ( please refer to: “https://www.youtube.com/watch?v=cNQq53bbgQI&t=169s” ). Set on each disk two partitions with CONSTANT SIZE. Firstly delete every past partition on disks ( please make sure, that data is copied, and there are connected, disk meant only for erasing ).
Raid space1:
Use as: “physical volume for RAID”
Type for Swap: “primary”
From beginning
Raid space2:
Use as: “physical volume for RAID”
Type for operating system: “logical”
beginning
Configure software RAID->Create MD Device -> RAID 0, and check with space:
space1 disk partitions Raid 0 – for boot
space2 disk partitions Raid 0 – for swap
space3 disk partitions Raid 0 – for operating system
Created RAID 0 disks set to:
space1 Raid 0 Use as: “EFI”
space2 Raid 0 Use as: “swap area”
space3 Raid 0 Use as: “Ext4 journaling file system”;
Mount point: “/ - the root file system”
DUALBOOT
Dual boot configuration could not be detected with usage of “update-grub” command. It is connected with RAID configuration. To enable this edit “/etc/defatult/grub” and add:
GRUB_DISABLE_OS_PROBER=false
and execute:
sudo os-prober && sudo update-grub

Post Scriptum: if one is not sure, he or she should physically disconnect essential disk devices.