GCC ARM
Vast set of ARM processors can be easily programmed with usage of GCC ARM tool. This tutorial is intended for Cortex M4 with float coprocessor ( armv7-m + f uarch )
1) install package, or compile from sources:
#sudo aptitude install gcc-arm-none-eabi
2) write some source:
#vim a.c
#define RAM_END	0x20003FFF
int main( void );
unsigned long* vector_table[] __attribute__((section(".vector_table"))) =
{	( unsigned long* )RAM_END,	//initial SP
( unsigned long* )main	//Reset_Handler
};

int main()
{	while( 1 );
};

3) write processor-specific linker file:
#vim stm32_CM4F.ld
MEMORY	/*stm32F373x8*/
{	FLASH	(rx)	:	ORIGIN = 0x08000000, LENGTH = 64K
RAM	(rwx)	:	ORIGIN = 0x20000000, LENGTH = 16K
};

SECTIONS
{	.vector_table	:
{	*(.vector_table)
} > FLASH
.text	:
{	*(.text)
} > FLASH
.data	:
{	*(.data)
} > RAM
};
4) write run commands BASH script:
#vim RUN_COMMANDS.sh && sudo chmod +x RUN_COMMANDS.sh
#!/bin/bash
GCC_GENERAL='-c'
GCC_OPT='-O1 -Wall'
GCC_ARCH='-mcpu=cortex-m4 -mthumb'
GCC_FLOAT='-mfloat-abi=hard -mfpu=fpv4-sp-d16'
GCC_DEBUG=''
L_FILE='stm32_CM4F.ld'
L_FLAGS='-nostartfiles --print-map'

FILENAME='a'
clear &&
arm-none-eabi-gcc $GCC_GENERAL $GCC_OPT $GCC_ARCH $GCC_FLOAT $GCC_DEBUG $FILENAME.c -o $FILENAME.o &&
arm-none-eabi-ld $L_FLAGS -T$L_FILE $FILENAME.o -o $FILENAME.elf	&&
arm-none-eabi-size -tA --radix=16 $FILENAME.elf	&&
arm-none-eabi-objcopy -Oihex $FILENAME.elf $FILENAME.hex	&&
touch $FILENAME.elf $FILENAME.o && rm $FILENAME.elf $FILENAME.o