LINK AGGREGATION / BONDING
1) if one has a multiple GbE interfaces ( 1 from motherboard MB and additional one port from PCI network card ) he or she will be able to get one connection of multiplyied identical interfaces. Of course there must be at least two Personal Computers with 2 GbE ports via MB and PCI card. At beginning install:
#sudo apt-get install ifenslave
2) manage network connection configuration for 1+1GbE with higher MTU value for sending big files ( > few MB ) on each side:
#vim /etc/network.interfaces
auto lo
iface lo inet loopback

auto enp0s1	#ordinary network config
iface enp0s1 inet manual
address 192.168.150.3
network 192.168.0.0
netmask 255.255.0.0
gateway 192.168.150.1
dns-nameservers 8.8.8.8 8.8.4.4

auto eno2
iface eno2 inet manual
bond-master bond0

auto eno1
iface eno1 inet manual
bond-master bond0

auto bond0
iface bond0 inet static
address IPv4Addr
netmask 255.255.0.0
bond-mode 0
bond-miion 100
bond-lacp-rate 1
bond-slaves eno2 eno1
mtu 9000
3) note that eno 2 and eno1 are names of network interfaces ( one can list them with ifconfig command )
4) restart connection:
#sudo ip addr flush IPInterfaceName && sudo systemctl restart networking.service	&& sudo service networking restart && sudo service network-manager restart
5 test connection speed:
# sudo apt-get install iperf
    at iperf server side run listening:
#iperf -s
    at iperf testing client side run measures:
#iperf -c IPv4Addr